## Slide 1
KTH Edge AI
Robotics Challenge
Kick-off meeting
2026.10.07

## Slide 2
Challenge overview
02
Each team will control a group of approximately four wheeled mobile robots operating in an unknown indoor environment. During the mission, the robots may need to:
Explore an initially unknown environment
Detect, identify, and localize different targets
Share information between robots and edge node
Allocate tasks among robots
Form robot groups to complete specific rescue tasks
Adapt their behavior according to mission updates
Manage computation, communication, or energy consumption
Core theme: AI + Robotics + Edge Computing + Communication + Control

## Slide 3
System architecture - overview
03
1. Mobile robot team
Robots perform sensing, local computation, motion control, and exploration.
Robots can communicate and share local information with each other.
2. Edge computing node
A single local computing server is available to each team.
Teams decide which tasks are executed onboard and which are offloaded to the edge.
Typical edge functions may include: multi-robot coordination; perception/object detection; map fusion; task allocation; LLM inference.
3. Human operator + LLM
The human operator provides natural-language mission updates.
The LLM interprets the instructions and converts them into executable tasks.

## Slide 4
Competition environment
05
Illustrative arena
In-door, flat-floor environment of approximately 5m × 5m (final dimensions are TBD), containing rooms, walls, and static obstacles.
Rescue targets are represented by ArUco visual markers and divided into two types: Normal Targets and Cooperative Targets.
Rescue zone is used for rescue-completion verification. Each ArUco marker corresponds to one or more predefined Rescue Zones.
A rescue is completed when the robot enters the corresponding Rescue Zone and remains there continuously for the required duration.

## Slide 5
Overall competition flow
05
Task 1
Explore, map
and detect
Handover
Save unified
outputs
Task 2A
Autonomous
rescue
Safe Mode
Verify results and reposition
Task 2B
LLM-guided
mission
Two main tasks

## Slide 6
Task 1 Autonomous exploration, mapping, and detection
06
Teams may use up to two robots starting from a designated start area to autonomously explore an unknown environment and build a unified 2D occupancy grid map within limited time:
The robot system shall operate autonomously based on the current map and sensor information, performing path planning, obstacle avoidance, and motion execution toward the selected target;
Existing ROS 2 SLAM, navigation, and other open-source software packages are allowed.

## Slide 7
Task 1 Autonomous exploration, mapping, and detection
06
Teams may use up to two robots starting from a designated start area to autonomously explore an unknown environment and build a unified 2D occupancy grid map within limited time:
The robot system shall operate autonomously based on the current map and sensor information, performing path planning, obstacle avoidance, and motion execution toward the selected target;
Existing ROS 2 SLAM, navigation, and other open-source software packages are allowed.
Target detection and localization
The system shall perform the following pipeline:
01
ArUco observation
02
Identify target ID and type
03
Pose in
map frame
04
Update
target list
Estimate relative position
05
Required output: A 2D occupancy map and a target list

## Slide 8
Task 2A Multi-robot rescue
08
Task 2 uses the unified map and target list generated in Task 1. Multiple robots cooperate to complete rescue tasks. Teams may use up to four robots and use the organizer-provided edge node for global state aggregation, task planning, and multi-robot coordination.
Task 1 Outputs
Unified Map
ID Type
T1 Normal
TC1 Coop.
Target List
Map + target information from Task 1
Edge Node
Task assignments
State / progress
Task planning – What should be done next?
Robot allocation – Which robot(s) should do it?
Coordination – How should robots cooperate?
Global state – Track progress and update plans
Multiple Robots
Autonomous Navigation & Rescue Execution (path planning, motion control, obstacle avoidance)
Design the robot–edge communication interface
Build global robot and target state management
Develop task planning and robot allocation
Teams develop
Implement multi-robot coordination
Integrate task assignments with autonomous navigation and rescue execution

## Slide 9
Normal and cooperative rescue
09
Normal Target
Cooperative Target
Rescue Zone
Zone A
Zone B
1 robot
Continuous dwell
2 different robots
Simultaneous continuous dwell
Rescue zone position is determined from the marker pose using unified and publicly specified geometric rules (TBD)
Task 2A is also time-limited and ends when one of the following conditions occurs: (1) The competition time limit is reached; (2) All valid rescue targets have been successfully completed; (3) The referee terminates the run due to safety, equipment failure, or another necessary reason.
After Task 2A results have been verified, the organizers will reposition the robots to predefined Task 2B starting positions. The map, target list, and other environment information obtained previously are retained.

## Slide 10
Task 2B LLM-guided mission: Task flow
11
In this task, the LLM acts as a high-level mission interpreter and planner. Its primary role is to understand the natural-language mission instruction and convert mission objectives and high-level constraints into a structured mission plan.
Edge Node
Task assignments
State / progress
Multiple Robots
Autonomous Navigation & Rescue Execution
Operator
Natural-language mission input
LLM Mission Interpreter
Interpret instruction，Extract objectives & constraints， Generate a structured mission plan
Multi-Robot Coordinator
Execution planning ，Robot allocation，Coordination，
Global state management
Structured mission plan
Natural-language mission input interface
LLM prompting and mission interpretation
Structured mission-plan representation
Teams develop
Integrate the LLM mission layer with the existing Task 2A coordination framework
Retained
information

## Slide 11
Task 2B LLM-guided mission: Task flow
11
In this task, the LLM acts as a high-level mission interpreter and planner. Its primary role is to understand the natural-language mission instruction and convert mission objectives and high-level constraints into a structured mission plan.
Edge Node
Task assignments
State / progress
Multiple Robots
Autonomous Navigation & Rescue Execution
Operator
Natural-language mission input
LLM Mission Interpreter
Interpret instruction，Extract objectives & constraints， Generate a structured mission plan
Multi-Robot Coordinator
Execution planning ，Robot allocation，Coordination，
Global state management
Structured mission plan
Retained
information
Simple Example
Natural-language mission
“Rescue T2 first. Then T1 and T3. Complete TC1 last.”
LLM → Structured mission plan
T2 → {T1, T3} → TC1
Coordinator / Robots
Robot assignment, navigation, coordination and rescue execution

## Slide 12
Robot platform and development environment
04
The competition uses differential-drive wheeled mobile robots:
Differential-drive platform
Wheel encoders
Mobile Base
Perception
RPLIDAR — mapping & obstacle sensing.
RealSense D435i — RGB-D perception & ArUco detection
State Estimation
Wheel encoders
IMU
Odometry/localization support
Onboard Computing
Intel NUC11TNKi5
NVIDIA GT 1030
ROS 2 onboard software
More information about the robot can be found at: https://canvas.kth.se/courses/59505/pages/robot-setup?module_item_id=1339720
Edge node information to be announced later…

## Slide 13
Robot platform and development environment
04
Environments used to develop, test, integrate, and deploy the challenge system:
1. Robot & Edge computing
• Ubuntu Linux
• ROS 2
• Python / C++
• ROS 2 workspace & package system
Provides the common runtime and development environment for robot-side and edge-node applications.
2. Simulation environment
• Gazebo
• Simulated robot model
• Simulated indoor competition arena
• Simulated LiDAR/RGB-D sensors
Enables autonomy and multi-robot behaviors to be developed and tested before physical deployment.
3. Communication environment
• Local Wi-Fi/LAN
• ROS 2 DDS communication
• Topics / services / actions
• Robot IDs and namespaces
Supports communication between robots, the edge node, and the operator, including task dispatching, state sharing, feedback, and coordination.
4. Development & Debugging
• RViz
• ROS 2 CLI & colcon
• rosbag
• Git / VS Code / terminal tools…
Supports visualization, debugging, data recording, software integration, and team collaboration.
Task 2B add-on: LLM inference runtime and model on the edge node — exact backend/model to be specified later.

## Slide 14
What we provide vs. What teams develop
Organizer Provides
Teams Develop
Status:
Available
Partial
To do
Available
Robot platform & onboard hardware
Available
ROS 2 / Gazebo development environment
Available
Basic robot model for Gazebo simulation
Available
Simulated sensor / Single-robot SLAM baseline
Partial
Basic setup/ simulation tutorial
Partial
Competition task/ arena / target specification
Real-robot ROS 2 I/O interface
Robot-edge basic network connectivity
To do
Edge-node base runtime / LLM environment
• Autonomous exploration and navigation integration
• Target detection and localization
• Robot–edge communication and information sharing
• Global robot / target / task-state management
• Task planning and robot allocation
• Multi-robot coordination and cooperative rescue
• Feedback, failure handling, and replanning
• LLM mission interpretation and integration for Task 2B
• Overall system integration and testing
To do
To do

## Slide 15
Milestone and development timeline
13
End-to-end autonomous rescue baseline (simulation demo is sufficient)
Autonomous exploration, ArUco detection and localization
Autonomous map-based navigation
At least two robots should connect, with their states available to the system
Basic robot–edge communication demonstrated
Basic task planning and robot allocation
At least one Normal Rescue and one Cooperative Rescue
Week 0
Kick-off
Week 4
Mid-term milestone
Week 8
Final
Early Development Phase
Integration and real-robot validation
• Focus primarily on Gazebo simulation
• Develop and test exploration, SLAM, navigation, multi-robot coordination…
• Use simulation for rapid iteration and debugging
• Physical robots are used mainly for validation and system integration
• Teams that need real-robot testing should book a time slot in advance

## Slide 16
Resources and next steps
14
Resources
Rulebook v0
Robot Setup and Technical Tutorial
ROS 2 workspace and Gazebo resources
After this meeting
1 Set up and run the simulation
2 Check interfaces and SLAM
3 Implement autonomous exploration
4 Assign team responsibilities
Questions and discussion